## Slide 1: Terracing
Slowing down water and minimizing soil erosion

## Slide 2: Problem: Design a solution
Your team is a farmer, engineer, and soil scientist.
Can you find a solution to this problem?

## Slide 3: Why Terraces?
Reduce rate of runoff and allow soil particles to settle, cleaner water is carried off in a non-erosive manner
Used on farmland with uniform, moderate slope
Terraces collect water and store it until it can infiltrate into the ground or be released through a stable outlet like an underground pipe
Terraces channel and slow runoff water and carry it to a stable outlet like a grassed waterway
Terraces must fit the contour of the land
Grassed terraces can provide increased habitat for birds and other wildlife

## Slide 4: Terracing
https://youtu.be/BBLgvN9jA8g

## Slide 5: Types of terraces
Grassed back slope
  Grass slope on one side, farmed on one side
  Benefit: used on slopes greater than 6%
Photo courtesy of USDA-NRCS, Iowa

## Slide 6: Types of terraces
Narrow base
  Grass slopes on both sides
  Benefit: used on slopes greater than 6%
Photo courtesy of USDA-NRCS, Iowa

## Slide 7: Types of terraces
Steep front, farmable backslope
  Should not be built on slopes greater than 6%
  Benefit: less ground out of production
  Benefit: less maintenance
  Benefit: less expensive than broad base
Photo courtesy of USDA-NRCS, Iowa

## Slide 8: Types of terraces
Broad base
  Flatter looking, farmed on both sides
  Should not be built on slopes greater than 6%
  Benefit: Entire terrace can be farmed
Photo courtesy of USDA-NRCS, Iowa

## Slide 9: Types of terraces
Broad base
  Flatter looking, farmed on both sides
  Should not be built on slopes greater than 6%
  Benefit: Entire terrace can be farmed
Photo courtesy of USDA-NRCS, Iowa

## Slide 10: Terracing
https://youtu.be/UxHYwrBIyZ8